## Slide 2: Dynamic Obstacle Avoidance
When unexpected obstacle appear in robots’ environment.
  Static obstacles which block the exiting path
    Take action: DWA, APF, VO…
  Moving obstacles with unknown intention
    Make prediction or risk analysis of dynamic obstacle
    Take action

## Slide 3
When unexpected obstacle appear in robots’ environment…
Static obstacles which block the exiting path
Moving obstacles with unknown intention
Make prediction or risk analysis of dynamic obstacle
Take action: DWA, APF, VO…

## Slide 4: 當機器人遭遇預期之外的障礙物時
如果是新的靜止物體阻擋了預先規畫好的路徑
  直接採取避開障礙物的行動
如果是會移動的物體出現在環境中，則需…
  預測動態障礙的行為
  評估環境及自身行動的風險
  再做出避開障礙物的行動
RRT事先規劃好的路徑
For example:

## Slide 5: 預測動態障礙(人類駕駛)的行為
建立駕駛行為的機率模型
得到互動車輛煞車/讓道的機率
獲取參數
蒐集數據分析駕駛行為的特徵參數
辨識不同駕駛的特徵參數差異
駕駛反應時間TFA(time for reaction)
基於特定路口的駕駛行為，建立預測用的機率模型
反映出不同駕駛的行為差異
駕駛讓行機率POY(probability of yielding)
將機率資訊提交給自駕車的決策系統

## Slide 6: 評估動態環境的風險
兩車中心連線距離減去各自的蛋形碰撞半徑後可以得到兩車間距。
將此間距乘以指數分布後，便可得到呈指數分布的碰撞風險機率。
建立指數分布模型
分析 車輛/路線/環境 風險
分析特定工況風險
跟車行為:
超車行為:
左轉行為:

## Slide 7: 避開動態障礙物
改善傳統DWA(Dynamic Window Approach)方法僅能將移動中的物體視為靜態障礙的困境
問題: 無論是為動態物體的位置施加小或大的膨脹層，依然都有可能碰撞
加入預測層後，為機器人帶來更聰明的避障方式